## Slide 1
April Novak
Assistant Professor
Nuclear, Plasma, and Radiological Engineering (NPRE)
University of Illinois, Urbana-Champaign
Workshop

## Slide 2: Welcome
Provide introduction to Monte Carlo methods and how to use OpenMC
Understand the unique features and advantages of OpenMC relative to other software
Have an enjoyable time!

## Slide 3: Logistics
Instructor
  Prof. April Novak (ajnovak2@illinois.edu)
Google Collab
  Check your email for URL link

## Slide 4: Workshop Timeline
Introduction to Monte Carlo theory
Introduction to OpenMC
OpenMC examples (interactive)

## Slide 5: Google Collab Instructions
Step 1:
  Open the google collab notebook via the URL sent to your email;
  Press "File" in the menu bar and then "Save a copy in Drive";
Step 2:
  The first cell needs to be run alone, because it will restart the kernel;
  "Your session crashed for an unknown reason" will show at the bottom, just close it;
  Run the second kernel and you are good to go.
Two versions of the notebook are available:
  “Solutions” with all text populated
  “Empty” for you to type along

## Slide 6: Neutron Physics 101

## Slide 7: Scattering

## Slide 8: Capture

## Slide 9: Fission
Produces very high-energy neutrons (2 MeV  246 million mph)
Fission reaction is most likely at low energy (0.000000025 MeV)
Energy released is converted into heat
Highly radioactive, these also generate energy (later)

## Slide 10: The Neutron Transport Equation

## Slide 11: The Neutron Transport Equation
Neutron flux: how many neutrons at a given location?
Cross section: probability* a neutron undergoes a particular interaction
*per distance traveled

## Slide 12: The Neutron Transport Equation
LOT of unknowns

## Slide 13: The Neutron Transport Equation
LOT of unknowns
VERY complicated functions of energy

## Slide 14: The Monte Carlo Method
We cannot predict with 100% certainty what happens to an individual neutron (random processes)
We can predict well what happens to a large collection of neutrons using statistical methods
  Nuclear reactors have HUGE numbers of neutrons (108/cm3)
Monte Carlo methods: statistical solution to the neutron transport equation
Sample distance to next collision
Sample type of collision
Sample outgoing energy, direction
and count the # fissions!

## Slide 15: Neutron Transport Methods
Deterministic | Stochastic
Neutron Transport Equation is solved | Individual particles are tracked and averaged in a random walk directed by probabilities
Approximate geometry | Exact Geometry
Multigroup | Continuous and multigroup
Global numerical solution | Tallies
Shorter simulation times | Longer simulation times?
Parallelization is more challenging | Parallelization is easy

## Slide 16: Neutron Transport Problems
Fixed Source Problem
Eigenvalue Problem
  Pressurized Water Reactor
  (image credit: P. Romano)
  Radiation Shield
  (image credit: E. Yilmaz)

## Slide 17: Random Process
Discrete | Continuous
Coin
Flip
n
N
Reaction
Type
Response
Time
n
Distance To
Next Collision

## Slide 18: How can we simulate a random process on computer?

## Slide 19: Random Numbers
Random Numbers: sequence of numbers that have the special characteristic that it is not possible to predict based on the previous numbers in the sequence.
Physical Random Number Generator | Pseudorandom number generator
 | An algorithm for generating a sequence of numbers whose properties approximate the properties of sequences of random numbers. Ex:

## Slide 20: How can we convert the random number into a random variable?

## Slide 21: Sampling (Discrete)
Flipping a coin
Generate a random number () between
if ( < 0.5)
else
Sampling Reaction Type
Generate a random number () between
if
else

## Slide 22: Sampling (Continuous)
Distance to next collision
Let be the PDF of the distance to next collision.
Let be the corresponding CDF.
Let be the PDF of the random numbers generated.

## Slide 23: Let’s simulate a neutron random walk

## Slide 24: Neutron Random Walk
Generate Neutron
Update velocity
Scattered
Move to surface
leaked
Move to collision site
dcollision< dsurface
yes
no
yes
no
(absorbed)
yes
Some more checks
no
leaked
Vacuum

## Slide 25: Criticality Algorithm
Guess initial source distribution
for i in n_cycles:
  Sample N neutrons from the neutron bank
  for j in N:
    Simulate the neutron until it get absorbed or leak from the system
    if (absorbed)
      Sample number of neutrons emitted per absorption
      Save these neutrons in the neutron bank
Compute

## Slide 26: Where are the results?

## Slide 27: Tallies
Tallies are normalized to be per source particle
Tallies examples:
  Flux
  Current
  Reaction rates
  Energy deposition

## Slide 28: Tally Example
Shield

## Slide 29: Statistics
Mean
Variance
Relative Error
Why MC is bad?

## Slide 30: Questions?